## Slide 2
MFLi3000 Quick Start Guide
Press here to continue

## Slide 3
The options below shows the inspection procedure with the MFLi3000.
Please click on one of the following guides to get started:
MFLi3000 Quick Start Guide
Starting a new inspection
Performing an MFLi3000 calibration
Performing a Freescan
Analysing a Freescan
1.
2.
3.
4.
X

## Slide 5
1. Starting a new inspection
Press here to continue

## Slide 6
To begin a new inspection process, press the New Inspection button.
Press
here to continue

## Slide 7
Complete the Inspection Details by pressing on each of text boxes. The keyboard will automatically appear.

## Slide 8
Press Continue to create the new inspection.
This will then take you back to the main menu.
Finish

## Slide 10
2. Performing an MFLi3000 calibration
Press here to continue

## Slide 11
Yes
No
Select plate and coating thickness
Perform calibration
Press ‘Calibrate’ on main screen
Adjust gain
Acceptable Calibration?
Set thresholds
Save calibration
The diagram below outlines the calibration procedure.
Press
here to continue

## Slide 12
Yes
No
Select plate and coating thickness
Perform calibration
Press ‘Calibrate’ on main screen
Adjust gain
Acceptable Calibration?
Set thresholds
Save calibration
The diagram below outlines the calibration procedure.

## Slide 13
Calibration Procedure
Yes
No
Select plate and coating thickness
Perform calibration
Press ‘Calibrate’ on main screen
Adjust gain
Acceptable Calibration?
Set thresholds
Save calibration
The calibration process begins here…

## Slide 14
Yes
No
Select plate and coating thickness
Perform calibration
Press ‘Calibrate’ on main screen
Adjust gain
Acceptable Calibration?
Set thresholds
Save calibration
This will bring you to the main calibration screen.
Then press Calibrate.
Calibration Procedure

## Slide 15
Yes
No
Select plate and coating thickness
Perform calibration
Press ‘Calibrate’ on main screen
Adjust gain
Acceptable Calibration?
Set thresholds
Save calibration
Select the appropriate plate thickness and coating. This will adjust the MFLi3000 gain automatically.
Press Accept to continue.
Calibration Procedure

## Slide 16
Yes
No
Select plate and coating thickness
Perform calibration
Press ‘Calibrate’ on main screen
Adjust gain
Acceptable Calibration?
Set thresholds
Save calibration
To perform a scan:
Ensure the MFLi3000 is set up correctly (check sensor height),
Position the MFLi3000 at the start of the calibration plate,
Select Start Scan,
Calibration Procedure

## Slide 17
Yes
No
Select plate and coating thickness
Perform calibration
Press ‘Calibrate’ on main screen
Adjust gain
Acceptable Calibration?
Set thresholds
Save calibration
To perform a scan:
Ensure the MFLi3000 is set up correctly (check sensor height),
Position the MFLi3000 at the start of the calibration plate,
Select Start Scan,
Then, turn the right hand Drive handle,
Note: The MFLi3000 must travel at least
6½ inches or 160 mm (a short scan warning will appear if distance not travelled).
Calibration Procedure

## Slide 18
Yes
No
Select plate and coating thickness
Perform calibration
Press ‘Calibrate’ on main screen
Adjust gain
Acceptable Calibration?
Set thresholds
Save calibration
After the scan, check the Calibration and decide if it is acceptable.
Calibration Procedure

## Slide 19
Yes
No
Select plate and coating thickness
Perform calibration
Press ‘Calibrate’ on main screen
Adjust gain
Acceptable Calibration?
Set thresholds
Save calibration
When Calibration traces are acceptable, continue to set / adjust thresholds.
If Calibration is not acceptable, Select Calibrate and repeat the calibration process. The gain values can be readjusted here.
Calibration Procedure

## Slide 20
Yes
No
Select plate and coating thickness
Perform calibration
Press ‘Calibrate’ on main screen
Adjust gain
Acceptable Calibration?
Set thresholds
Save calibration
Set the Reporting (Autostop) Threshold - blue line
Set the MFLi Threshold - green line
Calibration Procedure
Set the MFLi Threshold slightly lower than the Reporting Threshold, this will ensure that important signals are not missed.
Use the sliders to set Reporting and MFLi Thresholds.

## Slide 21
Yes
No
Select plate and coating thickness
Perform calibration
Press ‘Calibrate’ on main screen
Adjust gain
Acceptable Calibration?
Set thresholds
Save calibration
After the two Thresholds have been set, the calibration can be saved.
Enter meaningful calibration names to aid future identification.
Finish
Calibration Procedure

## Slide 23
3. Performing a Freescan
Press here to continue

## Slide 24
The diagram below outlines the procedure for MFLi3000 scanning. This section will guide you through this process.
Press
here to continue
Yes
No
Is reporting threshold correct?
Press ‘Scan’ to open the scan window
Press ‘Freescan’ on main screen
Adjust reporting threshold
Toggle Autostop on /off
Perform scan
View live trace whilst scanning
Press ‘Accept’ to close window

## Slide 25
The diagram below outlines the procedure for MFLi3000 scanning. This section will guide you through this process.
Yes
No
Is reporting threshold correct?
Press ‘Scan’ to open the scan window
Press ‘Freescan’ on main screen
Adjust reporting threshold
Toggle Autostop on /off
Perform scan
View live trace whilst scanning
Press ‘Accept’ to close window

## Slide 26
Yes
No
Is reporting threshold correct?
Press ‘Scan’ to open the scan window
Press ‘Freescan’ on main screen
Adjust reporting threshold
Toggle Autostop on /off
Perform scan
View live trace whilst scanning
Press ‘Accept’ to close window
Freescan Procedure
The Freescan process begins here…

## Slide 27
Yes
No
Is reporting threshold correct?
Press ‘New Scan’ to open the scan window
Press ‘Freescan’ on main screen
Adjust reporting threshold
Toggle Autostop on /off
Perform scan
View live trace whilst scanning
Press ‘Accept’ to close window
Freescan Procedure
Press New Scan.

## Slide 28
Yes
No
Is reporting threshold correct?
Press ‘Scan’ to open the scan window
Press ‘Freescan’ on main screen
Adjust reporting threshold
Toggle Autostop on /off
Perform scan
View live trace whilst scanning
Press ‘Accept’ to close window
Freescan Procedure
The Freescan window is then displayed. The live view MFL capture feature will appear here.
An Endview of the MFL signals as they are captured can be seen here.

## Slide 29
Yes
No
Is reporting threshold correct?
Press ‘Scan’ to open the scan window
Press ‘Freescan’ on main screen
Adjust reporting threshold
Toggle Autostop on /off
Perform scan
View live trace whilst scanning
Press ‘Accept’ to close window
Freescan Procedure
Note: To permanently change the Reporting Threshold enter the Calibrate window and move the blue Reporting Threshold as desired
For this scan, the Reporting Threshold can be changed here.

## Slide 30
Yes
No
Is reporting threshold correct?
Press ‘Scan’ to open the scan window
Press ‘Freescan’ on main screen
Adjust reporting threshold
Toggle Autostop on /off
Perform scan
View live trace whilst scanning
Press ‘Accept’ to close window
Freescan Procedure
When selected the MFLi3000 will stop if it receives an indication / signal response above the user set Reporting Threshold
To toggle the Autostop functionality (stop-on-defect), press the Autostop button.

## Slide 31
Yes
No
Is reporting threshold correct?
Press ‘Scan’ to open the scan window
Press ‘Freescan’ on main screen
Adjust reporting threshold
Toggle Autostop on /off
Perform scan
View live trace whilst scanning
Press ‘Accept’ to close window
Freescan Procedure
To perform a scan:
Ensure the MFLi3000 is set up correctly (check sensor height),
Position the MFLi3000 at the start of the area to be scanned,
Select Start Scan,

## Slide 32
Yes
No
Is reporting threshold correct?
Press ‘Scan’ to open the scan window
Press ‘Freescan’ on main screen
Adjust reporting threshold
Toggle Autostop on /off
Perform scan
View live trace whilst scanning
Press ‘Accept’ to close window
Freescan Procedure
To perform a scan:
Ensure the MFLi3000 is set up correctly (check sensor height),
Position the MFLi3000 at the start of the area to be scanned,
Select Start Scan,
Then, turn the right hand Drive handle,
Note: The MFLi3000 must travel at least
6½ inches or 160 mm.

## Slide 33
Yes
No
Is reporting threshold correct?
Press ‘Scan’ to open the scan window
Press ‘Freescan’ on main screen
Adjust reporting threshold
Toggle Autostop on /off
Perform scan
View live trace whilst scanning
Press ‘Accept’ to close window
Freescan Procedure
Live View Options
To aid corrosion identification the MFLi3000 user can toggle between Bi-Level and Gradient

## Slide 34
Yes
No
Is reporting threshold correct?
Press ‘Scan’ to open the scan window
Press ‘Freescan’ on main screen
Adjust reporting threshold
Toggle Autostop on /off
Perform scan
View live trace whilst scanning
Press ‘Accept’ to close window
Freescan Procedure
To aid corrosion identification the MFLi3000 user can toggle between Bi-Level and Gradient

## Slide 35
Yes
No
Is reporting threshold correct?
Press ‘Scan’ to open the scan window
Press ‘Freescan’ on main screen
Adjust reporting threshold
Toggle Autostop on /off
Perform scan
View live trace whilst scanning
Press ‘Accept’ to close window
Freescan Procedure
Press Accept to go to the Analysis screen .
Finish

## Slide 37
4. Analysing a Freescan
Press here to continue

## Slide 38
The diagram below outlines a typical procedure to analyse scans.
This section will guide you through this process.
Press
here to continue
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish
No
Yes
Indications above level?
Use zoom tools to navigate around indications
Check indications above MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Yes
No
Prove up required?
Move to area for prove up
Save scan as image?
Export scan if required
Next scan
Manual prove up
and marking

## Slide 39
The diagram below outlines a typical procedure to analyse MFL maps collected with the MFLi3000. This section will guide you through this process.
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish

## Slide 40
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish
Use the tools to quickly assess the scanned plate.
The first check is the Signals of Interest Indicator.
This shows the number of areas detected above the MFLi Threshold.

## Slide 41
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish
This is the Endscan tool. It is helps locate possible areas of corrosion.
The Endscan displays the MFL signal response along the scan. In the example here, three signals are shown to be above the MFLi Threshold, corresponding to the signals on the MFLi map.

## Slide 42
The Endscan also shows MFL signal amplitude compared with the baseline noise level.
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish
This helps in setting reliable threshold levels.

## Slide 43
For more detailed inspection on long scans use the zoom features.
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish

## Slide 44
The MFLi3000 has three different viewing modes
MFLi view for area sizing and characterisation
MFL view for checking unprocessed signals
STARS view for top side identification
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish
These views are used together to verify findings and identify if corrosion is located on the top or bottom side of the plate.

## Slide 45
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish
Touch an indication to show related information.

## Slide 46
You can also adjust the MFLi Threshold in this screen. This will provide a visual feedback in the Endscan view and on the MFLi map in the centre of the screen.
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish
Doing this will allow the user to identify discontinuity patterns and regions of interest.

## Slide 47
After analysing the data the user might decide that further prove up is required.
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish
If so, the MFLi3000 can be moved to the area of interest, and its position will be shown on the screen.

## Slide 48
To move the MFLi3000 to an area of interest either
Drag manually or
Drive forwards or backwards (drive options circled in green)
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish
When the MFLi3000 is moved the Image Marker (circled in blue) automatically updates both on the scanned track and in the Endscan

## Slide 49
If a reportable area is found, the user can Export (save) the scanned image.
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish

## Slide 50
No
Yes
Further analysis required?
Use zoom tools to navigate around indications
Check defects above MFLi threshold
Adjust MFLi threshold
Assess indications in different analysis modes (MFL, MFLi and STARS)
Hover cursor over indications
Yes
No
MFLi3000 reposition required?
Use MFLi drive motor controls
Save scan as image?
No
Export scan
Finish
If an image is exported, a description can be entered. This description is saved in a Freescan log file found in the inspection folder and can be viewed in Microsoft Word.
When an image is exported all three view options are exported – MFLi, MFL and STARS.
This completes the analysis procedure.
Finish